## Slide 1: Process Safety Management
Valerie Orr
Shazad Barghi
Ralph Buchal
Prepared for MINERVA November 2013

## Slide 2: Introduction
Module Outline
What is PSM?
Importance of PSM
PSM Systems
Rules, Regulations, and Guideline for PSM in Canada
References and further reading

## Slide 3
MODULE outline:
Process Safety Management
Description:
This module is meant to provide an introduction to process safety management (PSM). In a very simple sense, PSM is a framework for identifying and managing process risks. It is a type of safety management system that is specific for the process industries. Therefore, the principles are relevant to all disciplines of engineering involved in a process facility and are also broadly applicable to other manufacturing industries. The ultimate goal of PSM is to prevent the occurrence of major hazard incidents which are not appropriately addressed through traditional occupational health and safety procedures. This is due to the fact that many serious unplanned incidents are many times not simply attributable to any individual operator error. PSM strives to ensure all hazards of a process are identified and effectively managed for the lifetime of the process, regardless of changes in personnel, organization, or environment. The principles of PSM as taught in this module are based on a particular reference from the American Institute of Chemical Engineers Center for Chemical Process Safety (AIChE CCPS).

## Slide 4
Primary Reading Materials:
Risk Based Process Safety Management (2007)
Introduction to the twenty elements of PSM developed by the American Institute of Chemical Engineers Center for Chemical Process Safety
Safety Management: A comprehensive approach to developing a sustainable system (2012)
A comprehensive look at the factors that affect safety improvements and the effectiveness of a process safety management system. Large focus on the human factors which affect the adoptions of safe work practices, such as leadership and behavior.

## Slide 5
 | Chapter Title | Contents
1 | Introduction | The importance of PSM in the prevention of major hazard incidents Brief History and recent examples Rules and Regulations for PSM in Canada PSM Systems
Elements of Process Safety Management |  | 
2 | Commitment to PSM | Process safety culture Compliance Competence Workforce involvement Stakeholder outreach
3 | Hazard Identification and Risk Assessment | Hazard identification & risk management Knowledge management
4 | Risk Management | Operating procedures Training & performance Safe work practices Asset integrity & reliability Contractor management Management of change Operational readiness Conduct of operations Emergency preparedness
5 | Enhancing PSM | Incident investigation Auditing Metrics & measurements Management review

## Slide 6: What is Process Safety Management (PSM)?
PSM is the proactive application of management principles to a process for the prevention of loss of containment events
PSM is a system for dealing with:
“… human performance in complicated systems that involve inherent risk”
– Aviation Safety Expert and Pilot Chelsey Sullenberger
(Interview on the application of aviation systems safety lessons to medicine CBC Radio 2013)
This applies to the process industries too
Any site which stores, handles or manufactures hazardous substances or energy will have an inherent risk
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Process safety management (PSM) is the proactive application of management principles to a process for the prevention of process related injuries or incidents. PSM was created in response to several major hazard incidents which highlighted the need for a broader review process in order to prevent process-related incidents or injuries. Oftentimes, major incidents arising from process related events are beyond the control of a single operator and due to the complex nature of many processes, process hazards may not be as obvious as personal safety hazards. Thus, it is critical to have a framework to systematically address process hazards in every facility handling or storing hazardous substances.

## Slide 7: Loss of Containment
A loss of containment incident (LoC) occurs when a harmful substance or energy is released outside of the equipment which is meant to contain it [1,2,3,4]
  In some countries the amount of substance released dictates whether the incident is reportable to the government
  Also, in some countries, the amount of hazardous material contained in either equipment or at a facility can determine if implementation of PSM systems is required; e.g., Environment Canada Environmental Regulations, US OSHA PSM Rule 1910.119 [3, 5]

## Slide 8: Examples of PSM incidents
Faulty gauge causes an overfill of a storage tank spilling 10000 kg of ethanol
2000 kg of crude oil leaks from corroded piping
Operator opens process valve and causes acid spill and gets burned
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Microsoft image.

## Slide 9: Intent of PSM
PSM systems are meant for industries handling, storing, or manufacturing hazardous substances
Hazardous substances are defined by their reactivity, toxicity, flammability, or other dangerous properties by the Canadian Environmental Protection Act Part 8 Section 200 [5]
PSM is primarily intended for the process industries and is typically applied at a facility level
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: PSM is a systematic framework used to maintain the integrity of hazardous operations. Specifically it aims to eliminate loss of containment incidents that are more common in process facilities (Canadian Society of Chemical Engineering, 2012) (Energy Institute, 2010) (U.S. Department of Labor, 2000). Loss of containment incidents may have far reaching effects which are difficult to predict, and accordingly prevention is key. The consequences of loss of containment can range from the injury of an employee to serious harm or loss of life of the surrounding public.
Microsoft image.

## Slide 10: PSM is a Proactive Risk Based Approach
Proactive | Reactive
Implementing countermeasures to prevent an incident | Implementing countermeasures after an incident has occurred
Perform hazard analysis and risk assessment | Perform incident investigation and determine root cause
Practice inherently safer design | Design & install additional layers of protection after an incident
[1]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 11: PSM is a subset of system safety
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: PSM is a subset of systems safety engineering (SSE) and involves a combination of a safe engineering design, operational safety, and management principles as demonstrated in Figure. Other industries that handle high hazardous chemicals such as the transportation industry are governed by their own regulations and guidelines. These industries may also using very similar safety management systems to approach complex projects such as the aviation industry and the nuclear industry. Thus, risked based process safety management is applicable to many engineering disciplines.

## Slide 12
OCCUPATIONAL HEALTH & SAFETY |  | PROCESS SAFETY | 
Individual-oriented & controlled Focused on direct interaction between individual and equipment or structures Specific impact Work place rules & safety equipment Worker training & supervision |  | Cooperative Broad impact Systems Little individual control | 
Examples of Possible Incidents |  | Examples of Possible Incidents | 
Fall Spill Electrocution Asphyxiation Hearing Impairment and other chronic injuries Minor injuries (pinch, banged knee, etc.) |  | Explosion Release of hazardous chemical Fire Release of hazardous energy | 
Examples of Safeguards |  | Examples of Safeguards | 
Hazardous Work Permits Personal Protective Equipment Ventilation systems, confined space entry Guardrails, equipment guards |  | DESIGN | OPERATIONS
 |  | Pressure Safety Valves Inherently Safer Design Equipment Interlocks Process Alarms | Maintenance Inspections Training Procedures
[5,6, 7]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: PSM is meant to provide a systematic method of dealing with process warning signs and is not meant to replace traditional process safety elements. A properly functioning PSM system should consistently and effectively manage the process hazards throughout the entire process lifetime. Particular care must be taken for the management of change as well as developing an appropriate workforce culture. A well designed and implemented system can prevent the system from being circumvented or used in a perfunctory manner which may lull management into a sense of complacency (Center for Chemical Process Safety, 2008). Therefore, it must work in conjunction with existing standards of process safety, environmental compliance, product quality, Responsible Care commitments (Chemistry Industry Association of Canada, 2013), as well as occupational health and safety (OH&S) requirements (Government of Canada, 2013). This table clarifies the differences between OH&S and process safety

## Slide 13: Why is PSM Important?
PSM is important because loss of containment events in the process industries can have DIRE consequences for employees, the public, and the company.
Several major chemical catastrophes have demonstrated the need for effective PSM and the potential devastation of a dysfunctional system
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: PSM was created in response to several major hazard incidents. A major hazard incident occurs when containment of a hazardous material is lost. Loss of containment issues can have dire consequences not only for the people and places involved but also for the company operating unsafe facilities. PSM systems are important tools for dealing with the complexity of a process facility. Several major catastrophes demonstrate the importance of PSM and the potential consequences of dysfunctional systems.

## Slide 14: A few major industrial accidents
Incident | Effects
Bhopal, India, 1984 Union Carbide Methyl Isocyanate Release | >3800 fatalities, >100 000 injuries, severe damage to area livestock and crops, long term health effects, $470 M compensation
Chernobyl, USSR, 1986 Nuclear Reactor Meltdown | 30 acute fatalities, >130 000 people exposed to harmful radiation, long term health affects, permanent evacuation of the city
Gulf Oil Spill. USA, 2010 British Petroleum Deepwater Horizon Oil Platform Explosion and Spill | 11 fatalities from the explosion Extensive environmental damage, extensive damage to regional fishing and tourism industry, >$4.5 B USD in fines, >$42 B in civil settlements
Challenger Disaster, USA, 1986 NASA Explosion | Loss of crew (7 fatalities), loss of space shuttle (>$8 B USD), recovery of debris
[8, 9]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 15: Bhopal India, 1984
Union Carbide Corporation operating in Bhopal manufactured methyl isocyanate (MIC) as a precursor in Sevin (insecticide) production [8, 9].
Over >40 tons of MIC leaked into the air and caused over 3800 immediate fatalities and countless injuries and long term health affects.
Management had intentions to permanently shut down uneconomical operations and while many safety designs were not kept in operation even though a substantial MIC inventory was still in place
MIC tanks after Bhopal incident. (Wikipedia commons)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: The disaster that occurred in Bhopal, India is one of the worst process related disasters of all time. The short-term affects included over 2000 fatalities, 100 000 injuries, and significant damage to livestock and the surrounding environment (Atherton & Gil, 2008). The facility was built to manufacture the intermediary reagent methyl isocyanate (MIC) often used in the production of pesticides. The MIC was stored on site in two 57, 000 L tanks. A third additional 57,000 L tank was kept empty and reserved for emergencies. On the night of the accident, approximately 2000 L of water was introduced into one of the MIC storage tanks causing an exothermic reaction forming MIC vapour. Over the next two hours, over 40 tons of MIC was released into the atmosphere. Due to the nature of MIC, the toxic vapours remained close to the ground and spread into the neighboring community killing thousands. Several problems were later noted that would have been address had PSM or another hazard evaluation and management system been used. Accountability and corporate commitment to safety failed when supervisors failed to take immediate action when workers first reported a burning sensation in their eyes (Atherton & Gil, 2008). No management of change system was used to evaluate the effects of shutting down the safety equipment such as the refrigeration system and the soda scrubber. Equipment integrity and operating procedures were not maintained and as a consequence the pressure alarms had become so unreliable they were ignored by workers, the temperature alarms had failed to operate, and the tanks were filled beyond their recommended capacity (Atherton & Gil, 2008). Additionally, production had been halted for 6 months prior to the accident with the downstream pesticide plant using the stored MIC for an extended period of time indicating there was considerable amounts of this highly toxic chemical stored for an extended period of time. Inherently safer design dictates that inventory of highly toxic materials should be maintained at the lowest possible level to minimize the possibility of release.

## Slide 16: How did this happen?
On the night of the accident, approximately 2000 L of water was introduced into the MIC storage tanks causing an exothermic reaction to produce MIC vapours and increased pressure [8].
There is no consensuses on how the water was improperly introduced into the tanks. Some suggestions include valve malfunction or sabotage.
Regardless, safety considerations had been made in the design of the plant. The MIC storage tanks were equipped with a soda scrubber, a refrigeration system, and temperature and pressure alarms.
However, the scrubber was out of service. The flare, being the last defence, was also not in service.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 17: How did this happen?
Production had been halted 6 months prior to the accident and the downstream Sevin plant continued to operate using the stored MIC. This indicated that considerable amounts of MIC a highly toxic chemical was being stored for extended period of time.
Inherently safer design (ISD) dictates that inventory of highly toxic materials should be maintained at the lowest possible level to minimize the possibility of large releases. Also, newer technology was later developed to produce the same pesticide product without using MIC intermediate, thus employing the ISD principle of substitution.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 18: Why did this happen? (In terms of PSM)
Accountability and corporate commitment to safety failed when supervisors failed to take immediate action when workers first reported a burning sensation in their eyes.
No management of change system was used to evaluate the effects of shutting down the safety equipment such as the refrigeration system, the soda scrubber and the flare system while continuing to store a significant amount of MIC on-site.
Equipment integrity and operating procedures were not maintained and as a consequence the pressure alarms had become so unreliable they were ignored by workers, the temperature alarms had failed to operate, and the tanks were filled beyond their recommended capacity
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 19: Flixborough, UK, 1974
Napro UK located in Flixborough manufactured caprolactam a precursor for nylon synthesis [4,8,9,10].
An improperly designed bypass line caused the leakage of a 50 ton cyclohexane vapour cloud in seconds
Upon contact with an ignition source, the resulting explosion killed 28 employees and damaged over 1800 buildings in the surrounding area.
Allen, B. (2011). Flixborough: The price of nylon. Health and Safety at work.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Link to official report http://www.catastrophic-events.com/docs/Flixborough.pdf
Notes: One particular example that demonstrates the need for PSM systems is the accident in Flixborough, UK, 1974. Flixborough was a chemical process facility that produced caprolactam, a precursor for nylon synthesis. Prior to the accident, a crack was discovered in a reactor used for the oxidation of cyclohexane. In an effort to maintain production, it was decided to install a temporary bypass line. The bypass later ruptured and leaked approximately 50-60 tons of hot cyclohexane forming a massive vapour cloud (Center for Chemical Process Safety, 2008) (Kletz, 2009) (Health and Safety Executive, 1975). Upon contact with an ignition source, the resulting explosion decimated the plant, killing 28 employees and damaging 1800 buildings in the vicinity. The consequences would have been more disastrous if the explosion had occurred during a weekday as many more employees would have been onsite. Engineers’ onsite did not realize that special knowledge of high pressure, high temperature piping was required for safe design and operation of the bypass line. In this case, a PSM system would have required a management of change system which would have required the bypass to first be subject to approval by qualified personnel among other safety checks.

## Slide 20: How did this happen?
Prior to the accident, a crack in the reactor used for the oxidation of cyclohexane was discovered.
The maintenance engineer on-site decided to install a bypass line in order to maintain production and reduce down time.
However, the site experienced mechanical engineer had quit some time before, and those remaining decided to “fast track” a solution for the by-pass.
For design, they sketched a full-scale by-pass line in chalk on the maintenance shop floor.
However, no stress and thrust force analysis calculations were performed on the by-pass line.
The bypass later ruptured and leaked hot cyclohexane into the vicinity which ignited resulting in the explosion.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 21: Why did this happen? (In terms of PSM)
A functional PSM system would require a management of change system to deal with process design changes.
Every facility must ensure that competent personnel are hired and trained for the positions they fill.
Proper management of organizational change would have identified that the maintenance engineer, and the laboratory manager who also reviewed the shop floor sketch design, were unqualified
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 22: What are some of the consequences of major hazard incidents?
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: As the disasters at Flixborough and Bhopal illustrate, the consequences of major hazard incidents can be extensive. Not only can they cause serious loss of life, injury, and property damage, they can also seriously harm the environment and affect a company’s bottom line. In fact, serious loss of containment incidents can lead to financial crippling of a company. For example, the damage caused by the explosion of ethylene/isobutene in Pasadena Texas in 1989 caused over $800 million in damages (Turk & Mishra, 2013). The consequences of a serious hazard incident are summarized in the figure.

## Slide 23
Health and Safety | 
Workers are at highest risk of injury since they are at the “front line.” The public while not on-site is at risk when a serious major disaster occurs. | 
Worker | Death Severe injury Long term health problems Affects personal monetary success if injuries and health problems interfere with future work
Public | Death Severe injury Long term health problems Economic problems Community longevity Environmental health will also affect the public’s health and safety
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: The health and safety of individuals at a facility are on the front line of any incident, however, serious accidents have also killed or caused serious immediate and/or long term harm to the general public. It is the purpose of regulated engineering practice in Canada to protect the public through safe engineering design. Therefore, all engineers must be committed to increasing safety through risk-based process safety management.

## Slide 24
Environmental Impacts | 
Environmental damage caused by major disasters can harm residents’ health as well as lead to reduced longevity of the community | 
Atmospheric | Contamination of air quality used by humans, animals and vegetation Contamination of property (e.g. soot) Interference of normal quality of life and business
Aquatic | Contamination of water used for drinking, irrigation and recreation Harm to fish and wildlife
Terrestrial | Contamination of land and vegetation Property damage
[9]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Environmental damage caused by major disasters can harm residents’ health as well as lead to reduced longevity of the community. For example, tourism in the Florida panhandle and adjacent area came to a halt after the British Petroleum (BP) oil spill in 2010. Some economists estimate a loss of $22 billion dollars over three years in the gulf region and BP had to spend approximately $150 million dollars in marketing to rekindle the market (Oxford Economics, 2010). Accidents in agricultural areas can cause serious damage to livestock operations and crops.

## Slide 25
Corporate Losses | 
A major disaster can completely ruin a company. At minimum be severely detrimental to the well being of the organization and thus the employees | 
Clean Up | Clean up of the Deep Horizon spill & legal settlement fees cost >$14 B USD
Insurance | A poor safety record increases premiums on assets A poor safety record increases the number of health claims Large amounts of claim settlements cause higher premiums
Reputation | The international news reporting ensures the disaster will be seen by consumers around the world May cause consumer boycott Reputation as an employer that values safety
Productivity | Will decrease productivity and therefore profits if a facility is not operational
Product Quality | May decrease quality if facility is not operating at top quality May cause pressure on other facilities decreasing their quality
[11,13]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Finally, all of these effects will affect the company’s longevity. Clean-up efforts can be costly but are only a small portion of how these events can effect a company. Employee accidents can lead to a bad reputation as an employer decreasing productivity. Damage to the communities’ health, safety, and well-being can affect the publics’ image of the company and can affect productivity, employee morale, and attractiveness as an employer. Even minor incidents which affect operational integrity may affect product quality. Lastly, better safety history can lead to lower injury compensation pay-outs which in turn can affect insurance costs.

## Slide 26: The Elements of PSM
PSM systems are typically centered around four themes [4]:
Commitment of management and corporate objectives to PSM
Hazard assessment, including process knowledge and hazard identification
Risk management such as managing change in the process and change in personnel
Continuous enhancement such as furthering employee education and enhancing process knowledge
THESE ARE THE TITLES OF THE REMAINING SECTIONS OF THIS MODULE…. CLICK TO NAVIGATE
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 27: PSM System Possible Elements
[1, 2, 4]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 28
Two of the most important features of a PSM system are participation and communication
  Although PSM systems are typically designed by management they require input from operators and commitment from corporate executives to be implemented properly
PSM systems are non-prescriptive [13]
  They must be based on performance indicators to measure the success of the PSM system
  Guidelines can be implemented in many ways as long as the objectives are met
Finally, PSM systems are not created once and implemented once.
  They are an on-going process that involves auditing and revaluation of the management system to continually enhance the effectiveness of the PSM system.
  Risk is never zero.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Two of the most important features of a PSM system are participation and communication. Although PSM systems are typically designed by management they require input from operators and commitment from corporate executives to be implemented properly (Sutton Technical Books, 2013).
PSM systems are also non-prescriptive. They are accordingly based on performance indicators to measure the success of the PSM system. Guidelines can be implemented in many ways as long as the objectives are met. Finally, PSM systems are not created once and implemented once. They are an on-going process that involves auditing and revaluation of the management system to continually enhance the effectiveness of the PSM system. Risk is never zero.

## Slide 29: Process Safety Management Systems from around the world
  American Occupational Health and Safety Administration Process Safety Management Rule enacted in 1994
  14 Elements - CSChE – The Canadian Society for Chemical Engineering [1]
  20 Elements - AIChE CCPS – The American Institute for Chemical Engineers Center for Chemical Process Safety [4]
  12 Elements – OSHA – US Occupational Health and Safety Administration PSM Rule 1910.119 [3]
  20 Elements – EU Energy Institute [2]
  Some large corporations may also sell their custom systems or services for implementing PSM
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes:   There are several systems published and available on the web. Many of these systems were created by various international professional associations. The Canadian Society of Chemical Engineers (CSChE) recommends their 12 element system which is based on the 14 element system which is required by law in the United States. However, the American Institute of Chemical Engineering (AIChE) Center for Chemical Process Safety (CCPS) advocates for a more comprehensive 20 element system as the industry best practice. This 20 point system satisfies the minimum requirement of the 14 elements required by the American Occupational Safety and Health Administration (OSHA) and goes beyond to include more elements concerning corporate commitment to PSM and safety culture as well as future PSM enhancements. Generally they all contain the same elements under different categories names or varying in their comprehensiveness. For example, the OSHA PSM elements don’t cover safety culture in detail.

## Slide 30: Commitment to Best Practices
While no specific regulations to implement PSM in process facilities in Canada currently exist, nonetheless, “due diligence” does require companies to make their processes safe
Negligence or ignorance and failure to do a proper assessment to prevent an incident can be a criminal offense as described in the Criminal Code.
Bill C-45 – Amendment to the Criminal Code of Canada:
"217.1 Every one who undertakes, or has the authority, to direct how another person does work or performs a task is under a legal duty to take reasonable steps to prevent bodily harm to that person, or any other person, arising from that work or task.“ [14]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: While no specific regulations to implement PSM in process facilities in Canada currently exist, most companies are choosing to do so as industry best practice and as more data supporting the business case for PSM become available. The Chemistry Industry Association of Canada (CIAC) promotes PSM as part of their Responsible Care program for their members (Chemistry Industry Association of Canada, 2013).

## Slide 31: Westray Bill
Bill C-45 was passed as a result of the Westray Mine Explosion in Nova Scotia, 1992
About 8 months after the mine was opened, an underground methane explosion killed 26 workers who were underground at the time. There were no survivors underground [15].
A public inquiry found that the mine was poorly managed, worker safety was ignored, and poor oversight by the government regulators were the causes of the worse mining disaster in Canada
A criminal case was pursued against two managers but was dropped when it became unlikely they would be convicted.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 32: Responsible Care
The Chemistry Industry Association of Canada (CIAC) promotes PSM as part of their Responsible Care program for their members [6].
Many companies may possess facilities in the United States which are required by law since 1994 to have a functioning PSM system and are therefore experienced with the development and implementation of these systems.
http://www.canadianchemistry.ca/ResponsibleCareHome.aspx
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Opportunity to boast :) - Responsible Care designed and implemented first in Canada and now in 60+ countries around the world

## Slide 33: PSM around the world
  Two major international drivers of PSM:
  US OSHA PSM Standard 1910.119 [16]
    With the US OSHA levying hefty fines in the past few years, the need for functional PSM systems is increasing
  While no fines will be levied for failure to possess a functional PSM system in Canada, there are still legal requirements for all people directing work to take reasonable steps to ensure worker and public safety
  EU Seveso II Directive [17]
  Directive II was a revision of the original directive which increased the requirement to include a safety management system, as well as emergency and land-use planning

## Slide 34: PSM in Canada
In the event of a loss of containment, the criminal code of Canada states that there will be severe penalties for failing to ensure the safe operation of facilities and ensure operational integrity [14].
Environment Canada’s Environmental Emergencies regulation requires hazard assessments to prevent spills, which is the focus of PSM.
Ontario Environment Regulation 224 requires risk assessment of potential spills and a contingency plan
Alberta Strathcona County has bylaws requiring risk-based land use planning adjacent to hazardous
Other bylaws and regulations may exist and should be evaluated for every facility
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Many companies may possess facilities in the United States which are required by law since 1994 to have a functioning PSM system and are therefore experienced with the development and implementation of these systems. With the OSHA levying hefty fines in the past few years, the need for functional PSM systems is increasing (Busick). While no fines will be levied for failure to possess a functional PSM system in Canada, there are still legal requirements for all people directing work to take reasonable steps to ensure worker and public safety. In the event of a loss of containment, the criminal code of Canada states that there will be severe penalties for failing to ensure the safe operation of facilities and ensure operational integrity (Kelly, 2010).

## Slide 35: Summary
How do we prevent a loss of containment incident?
Maintain process integrity
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 36: References
1. Canadian Society for Chemical Engineering. Process Safety Management Guide. Ottawa : Canadian Society for Chemical Engineering, 2012.
2. Energy Institute. High Level Framework for Process Safety Management. London : Energy Institute, 2010.
3. U.S. Department of Labor. Process Safety: (OSHA 3132). s.l. : U.S. Department of Labor, 2000.
4. Center for Chemical Process Safety. Guideline for Management of Change for Process Safety. New York : John Wiley & Sons, Inc, 2008.
5. Government of Canada. Canada Environmental Protection Act, 1999. Environment Canada [Online] 07 10, 2013. http://www.ec.gc.ca/lcpe-cepa/default.asp?lang=En&n=E00B5BD8-1
6. Chemistry Industry Association of Canada. Responsible Care. Chemistry Industry Association of Canada. [Online] 07 10, 2013. http://www.canadianchemistry.ca/ResponsibleCareHome.aspx.
7. Government of Canada. Canada Occupational Health and Safety Regulations (SOR/86-304). Justice Laws Website. [Online] 07 10, 2013. http://laws-lois.justice.gc.ca/eng/regulations/SOR-86-304/.
8. Atherton, John and Gil, Fredric. Incidents that define process safety. Hoboken, NJ : John Wiley & Sons, Inc, 2008.

## Slide 37
9. Kletz, Trevor. What went wrong? Case histories of process plant disasters and how they could have been avoided. 5th. Oxford : Elsevier, 2009.
10. Oxford Economics. Potential Impact of the Gulf Oil Spill on Tourism. Washington : US Travel Association, 2010.
11. Health and Safety Executive. The Flixborough Disaster : Report of the Court of Inquiry. London : Her Majesty’s Stationery Office National Archives, 1975.
12. Turk, M.A. and Mishra, A. Process Safety Management: Going Beyond Functional Safety. Hydrocarbon Processing. [Online] 07 23, 2013. http://www.hydrocarbonprocessing.com/Article/3161534/Process-safety-management-Going-beyond-functional-safety.html.
13. Sutton Technical Books. Process Safety Management. Sutton Technical Books. [Online] 07 23, 2013. http://www.stb07.com/process-safety-management/process-safety-management-index.html.
14. Department of Justice, Government of Canada. Plain Language guide to Bill C-45. http://www.justice.gc.ca/eng/rp-pr/other-autre/c45/. Accessed: May 30, 2013.

## Slide 38
15. Government of Nova Scotia. The Westray Story: A predictable path to Disaster. http://novascotia.ca/lae/pubs/westray/. Accessed: June 2, 2013.
16. U.S. Department of Labor. Process Safety: Regulation 1910 : U.S. Department of Labor, 2000. [Online] https://www.osha.gov/pls/oshaweb/owadisp.show_document?p_table=STANDARDS&p_id=9760
17. European Commision. EU Seveso II Directive. European Commision , 2013 [Online] http://ec.europa.eu/environment/seveso/index.htm
18. Busick, Jennifer. Process Safety Management. SAFETY COMPLIANCE LETTER. pp. 5-6.
19. Kelly, Brian D. Process Safety Management and its impact on the professional engineering community. Calgary, Ontario, Canada : s.n., 2010

## Slide 39: Commitment to Process Safety
Process Safety Culture
Compliance with Standards
Process Safety Competency
Workforce Involvement
Stakeholder outreach

## Slide 40: Commitment to process safety
Evolution of organizational culture [1, 2]
  Confrontational/Enforcement
  ↓
  Cooperative/Collaborative
  Develop safety culture to consistently follow existing standards, involve the entire workforce and communicate with stakeholders
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Organizational safety has evolved over the years from a confrontational or enforcement relationship to a collaborative and cooperative relationship in the new millennium [1, 2].
It is now crucial for an organization to have an appropriate safety culture, follow existing standards, continuously increase their knowledge of PSM, involve the entire workforce, and provide a mode of communication for any stakeholder concerns

## Slide 41: Process Safety Culture
The way in which safety is managed and perceived in a workplace

## Slide 42: Process Safety Culture
The goals of a sound process safety culture are to [1]:
Monitor and maintain a sound safety culture
Support the consistent operation of the process
This is achieved by providing strong leadership and direction, prioritizing process safety, providing sufficient resources, and establishing performance standards and enforcing them.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Process safety culture describes an organization’s attitudes and behaviour towards PSM issues. It is the combination of group values which determine how process safety is managed (Center for Chemical Process Safety, 2011). It is an integral parameter in the successful implementation of a PSM system. Process safety culture should build on an already existing foundation of conventional safety culture. Operational procedures, expectations, and actual unsupervised behaviour are aligned in a sound process safety culture.

## Slide 43: What does a strong safety culture look like?
Weak Culture | Strong Culture
Assigns little value to process safety | Integrates process safety into the core values of the organization
Has poor sense of process safety vulnerabilities | Focuses on potential failures and strives to understand the risk and means of controlling it
Devotes minimal resources to process safety | Seeks to provide resources proportional to the perceived needs
Overlooks small indications of process safety problems | Places emphasis on learning from mistakes in order to prevent future problems
Accepts or normalized increasingly poor safety performance | Seeks to continuously improve process safety performance
Relies solely on few individuals or management to determine process safety hazards and risk management activities | Employees of all levels are involved in hazard identification and addressing the risks. Employees take action to address hazards at all levels
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[1]

## Slide 44: Organizational Culture
Tribal
Chaotic
Bureaucratic
Operational Excellence
People
Systems
STRONG
STRONG
WEAK
WEAK
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[3]

## Slide 45: Providing strong leadership
Strong leadership is required in order to establish process safety as a core value of the organization
An essential feature of good safety leadership is CREDIBILITY:
  What you say must be aligned with what you do
  Senior & middle management must be on the same page
  Executives and CEOs must possess strong will to make the right decision in the face of demands from shareholders and stakeholders
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: The importance of PSM for both the organization and the individual workers must be shared and reinforced on a regular basis (Frank, 2007). A deeply ingrained sense of respect for PSM should exist for all levels of the organization. Particularly, for engineers or engineers in training, it is an ethical imperative to place the safety of self, co-workers, and the public above employer or client desires.

## Slide 46: Providing direction
A balance of direction on production, facility, personnel, and safety must be given in order to prevent a reordering of priorities amongst middle managers and supervisors [2]
When leaders focus exclusively on production, this indirectly communicates that production should take precedence over everything else
This inhibits proactive preventive behaviours and encourages a reactive culture
What gets rewarded gets done
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 47: Establishing process safety as a core value
Engineers should always be reinforcing the organizations’ commitment to safety throughout their professional activities
“A practitioner [engineer] shall, regard the practitioner’s duty to public welfare as paramount” - Professional Engineers Ontario Code of Ethics [4]
A strong safety culture establishes a strong intolerance for any violations of safe practice in order to reinforce safety as a core value
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 48: Identifying your type of safety culture
Generative
Proactive
Reactive
Calculative
Pathological
“Who cares as long as you don’t get caught”
“Safety is only an issue if something happens”
“Safety is managed by procedures & documentation”
“Safety is managed by workforce involvement”
“Safety is how the business is run”
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[2]
Notes: Pictures from microsoft

## Slide 49: Leadership in process safety
Leadership is the most important variable in changing safety behaviours.
A good safety leader [2]:
  Prioritizes safety
  Sets safety targets
  Creates the safety vision
  Provides compelling direction
  Provides sufficient resources (such as people, time, money, or information)
  Weathers the impact of shareholder/stakeholder punishment on investments on improving safety and quality until it gains support upon maturity
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 50: Compliance with Standards
Following the law, rules, and regulations as well as any existing professional or design standards

## Slide 51: Compliance with standards
This is a fundamental requirement for organizations [5]
Relevant rules, regulations, and standards must be:
  Identified
  Understood
  Implemented or confirmed
Non-compliance typically results in fines but can also lead to serious accidents
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 52: Why should you comply?
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Because tragic accidents have taught us they could have been prevented if best practices were followed
Notes: This is a joke. To wake people up. The real answer is that experience has taught us to set engineering best practices, regulations, rules, and guidelines to reduce the chance of a serious accident. Photo from http://en.memory-alpha.org/wiki/Locutus_of_Borg

## Slide 53: What types of regulations & rules exist?
Licensing
Permit systems
Codes for equipment
  Pressure vessels
  Piping, etc.
Government requirements
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 54: Process Safety Competency
Process safety competency focuses on organizational learning. It is distinct from the training and knowledge elements which focus on cataloguing and storing information and maintaining worker competency respectively.

## Slide 55: What is the purpose of process safety competency?
The purpose of process safety competency is to proactively increase the body of knowledge of an organization prior to any incident occurring [1]
Additionally, this knowledge seeking must be supported by management and applications of newly acquired knowledge should be encouraged in order to reduce risk and increase process safety
The main purpose is to UNDERSTAND
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 56: Positive Learning Culture
Supports discussion and evaluation of divergent opinions and data
Stimulate new ideas
Recognize and accepts differences
Don’t depend only on incremental approaches to improve PSM
Maintains an external focus
Tolerating errors
Establishes and periodically updates the learning plan
Provide timely feedback
Ideas from outside the organization are not automatically discounted
Learns from errors. Failure to encourage innovation stifles improvement
Help focus the efforts to increase competence
Allow feedback on the means to improve how work activities are approached
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[1,6]

## Slide 57: Negative Learning Culture
Narrow focus and poor assumptions allow disruptive technologies
Filtering
Blind spots
Downplaying information that doesn’t fit in the existing paradigm
Lack of information sharing
Flawed interpretation
Inaction
Hoarding information and poor sharing
Poor logic due to lack of information or emotional bias
Unwilling or unable to act
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[1,6]

## Slide 58: Workforce Involvement
Involving all levels in the activities of process safety management

## Slide 59: Purpose of workforce involvement
The purpose of workforce involvement is engage employees of all levels in the development or revaluation of PSM elements
The workforce also includes and contract workers that will be affected by facility operations
Employees at different levels will contribute different information about the process that is necessary in order to create an effective PSM system
Frontline workers may be the best authority on day to day operations and routines
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 60: How to do you involve people in PSM?
Provide specific PSM responsibilities to their roles [1, 7]
Provide a mechanism for individuals to communicate their concerns or observations
Allow individuals to participate in protecting their own welfare
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 61: Benefits of workforce involvement
Individual empowerment [1,2]
  Everyone should feel they have a say in their own welfare and safety
Deference to expertise
  Recognize expertize or lack of it when evaluating process safety
Open communication
  Encourage participation in safety discussions
  May be that only 1 person realizes the risk
Mutual trust
  Foster trust between workers and management
Responsiveness
  Improve participation in safety by providing sincere timely response to PSM input or concerns
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 62: It applies to all elements!
Generally is involved in all aspects of PSM and not really specifically addressed by this element alone
Element specific activities may involve periodic opinion surveys
Evaluation of worker involvement
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 63: Stakeholder outreach
Providing a means of communication for the concerns of any stakeholders

## Slide 64: Who may be affected by your facilities operations?
Government Officials
Non-government associations
Emergency Response Services
Local councils
Politicians
Regulators
Fire
Paramedics
Police
Business/Industry associations
Environmental groups
Youth groups
Other
Residents
Post-secondary institutions
Local school boards
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Pictures from microsoft

## Slide 65: Why is stakeholder outreach an element of PSM?
Following the events of Bhopal, India, it was evident that the potential for damage to the surrounding community was immense and that chemical producers had an obligation to hear the concerns of the community
The Chemistry Industry Association of Canada (formerly the Canadian Chemical Producers Association) created a mandatory initiative called Responsible Care which calls for Community Awareness & Emergency Response practices
http://www.canadianchemistry.ca/ResponsibleCareHome.aspx
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Picture from website listed

## Slide 66: Goals of stakeholder outreach
The main objectives of the outreach element are to [1]:
Identify and engage the community and other stakeholders in discussions about process safety
Establish a mode of communication for any concerns of needs stakeholders may want addressed
Use the establish mode of communication to follow up on any aired concerns
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 67: Benefits of stakeholder outreach
Public discussion and openly addressing concerns builds trust with the stakeholders [2]
It is important for residents to feel confident that the organization is taking reasonable care to operate in a safe and environmentally sound way
Promoting transparency and responsiveness will increase the stakeholders confidence in the company [1]
This in turn may lead to the stakeholders willingness to cooperate in the future
Stakeholders will know how to contact the company should the need arise
TRUST
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 68: Who does this?
Communications personnel, phone operators, security guards, legal staff [1]
Key personnel should receive communications training in order to prepare them to hold planned events to press conferences
Legal personnel must give guidance to communications personnel in order to protect confidential business information while providing the appropriate information for any concern
Any additional staff such as those responsible for emergency response planning
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 69: Organizing your outreach system
How an organization pursues their outreach will depend on the size of the facility and the potential risks for the community [1]:
  Combine with other industrial partners in the area
  Emergency response may require a separate outreach format than other stakeholders
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes:   Some highly industrialized areas may chose to combine their outreach programs to report any stakeholder concerns to all facilities in the area and reduce the redundancy or complexity of operating many programs for the same stakeholder groups. The emergency response element requires input from the local emergency services and is mandatory, this element may follow a different outreach format that involves mainly emergency services staff which may be reported to the community using the outreach communication system

## Slide 70: Press Conferences
The outreach program will also be used in the aftermath of an incident should one occur [1,2]
By engaging the public in the outreach program prior to an incident, in a state of emergency, the public will already be aware of the communication plan of the facility
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 71: References
[1] Center for Chemical Process Safety. Guidelines for Risk Based Process Safety. New Jersey : Jon Wiley & Sons, 2011.
[2] Lutchman, C. et al. Safety Management: A comprehensive approach to developing a sustainable system. London: CRC Press,2012)
[3] Ian Sutton. (2010) Process Risk and Reliability Management: Operational Integrity Management. Elsevier.
[4] Professional Engineers Ontario Code of Ethics, Section 77 of the O. Reg. 941
[5] Energy Institute. High Level Framework for Process Safety Management. London : Energy Institute, 2010.
[6] Is yours a learning organization? Garvin, David A, Edmondson, C Amy and Gino, Francesca. 2008, Harvard Business Review, pp. 1-11.
[7] Canadian Society of Chemical Engineering. Process Safety Management Guide. Ottawa : Canadian Society of Chemical Engineering, 2012.

## Slide 72: Hazard and Risk Identification
Process Knowledge Management
Hazard Identification and Risk Analysis

## Slide 73: Hazard and Risk Identification
This pillar of PSM has two elements [1]:
  Process knowledge
  Hazard Identification and Risk Assessment
These two elements will form the bases of your risk management activities and therefore, comprehensive knowledge of your process and proper identification of hazards and their risks is crucial to PSM.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 74: 6. Process Knowledge
Identification and documentation of all relevant process knowledge for use in other PSM elements

## Slide 75: Process knowledge Management
This element boils down to three things:
  Understanding your process
  Documenting your understanding
  Managing the documentation process
The results of this element should be [1]:
  Accurate, complete, up-to date information about your process
  A documentation system
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 76: Process Knowledge
What kind of knowledge is necessary? [1]
  Chemical materials
    Hazard information, MSDS Sheets
  Reaction chemistry
    Kinetics, thermodynamics, calculations
  Process conditions
  Equipment design
    Design, fabrication and installation
  Engineering drawings & calculations
    Piping & Instrumentation Diagrams (PI&Ds)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: This is not a complete list. Just some of the more obvious ones. A process will likely need much more documentation

## Slide 77: Managing your documentation
Documentation and access of information is just as important as understanding your process [1]:
Information that is up to date must be protected
  Access must be protected to avoid inadvertent change
  Scheduling a cycle for updating documentation may help
Out of date information must be retrieved and controlled
  Access must be controlled to avoid circulation of incorrect knowledge
  Only kept for archival purposes
Knowledge must be documented in a usable and easily retrievable manner, a.k.a user friendly
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 78: Consequences of poor process knowledge management
Process knowledge is critical to identifying the hazards and risks of a process
Example: Hydroxylamine explosion, Pennsylvania 1999 [1]
  4 employee fatalities, 1 employee of an adjacent business killed
  14 injured, extensive damage to the area
Tom Volk, The Morning Call
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 79: Knowledge Translation
Very first pilot scale batch of hydroxylamine distillation in this facility
It was documented that hydroxylamine in solutions of >70% (w/v) undergo explosive decomposition
The process was designed to distill hydroxylamine to 85% (w/v)
Knowledge was not properly managed
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: It was documented in their very own MSDS from their lab scale studies.

## Slide 80: 7. Hazard Identification and Risk Analysis
Identify process hazards and evaluate process risks.

## Slide 81: Hazards & Risks
These terms are often used interchangeably, however they are not the same thing [1]
A hazard can be any chemical use, physical action, mechanical process, etc. that could, upon a failure event, cause damage to a person(s), property, or the environment
Risk is the probability that someone, property or the environment may suffer harmful consequences as a result of exposure to a hazard
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 82: Example: Car Accident
Car accidents
A car accident is a common physical hazard we have all seen. Lets specifically refer to one car hitting another car.
The risk of being in a collision is dependent on several factors; road conditions, driving ability, vehicle engineering design, etc.
However, in general, you might have (for example) a 1:1000 person chance of being in a collision.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Picture from microsoft

## Slide 83: Zero Risk
The only way to have zero risk is to never ride in a car so you can never be involved in a car/car collision.
The likelihood that you will never get in a car is pretty much zero (in Canada). So this is rarely true.
If a process is operating, the risk can never be zero. The only way to eliminate process risks is to never run the process.
You can’t lose if you don’t play!
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Picture from microsoft

## Slide 84: Severity or Consequences
The consequences will depend on your speed, road conditions, vehicle design, etc.
Therefore, the bigger the consequences the higher the risk.
  E.g. the faster you are going, the worse you could get hurt so you are taking a larger risk.
This is called the severity :
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Reference for information is from previous Minerva presentations on risk

## Slide 85: Increasing Risk
Two possibilities:
↑ probability = ↑ risk
  E.g. probability of a collision is higher in winter; so the collision risk is higher
↑ severity = ↑ risk
  E.g. the accident’s severity is worse if you don’t wear your seatbelt; so the collision risk is higher
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Difference between the risk of an event occurring vs. the risk to of a severe event occurring. Thus, a event that has low consequences but occurs very frequently (jamming your toe on a stair) could have a similar overall risk as an event that is unlikely but more severe (a fire). However, both pieces of information are important.

## Slide 86: Why is hazard identification important?
If you don’t know what the risks are, you can’t manage them!
What is the risk that the dealer has blackjack? Should you take the risk and bet? Does the risk change if the stakes are high?
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: The chances are 4/13 they have blackjack. If the stakes are high then your risk is higher because you have more to lose! Should you bet without knowing the chances?

## Slide 87: Risk
Incorrect hazard identification or risk assessment can lead to unknowingly accepting more risks than the company or community has deemed acceptable.
It can also waste time & money!
PERCEIVED RISK vs. ACUTAL RISK
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 88: Risk Assessment Matrix
The unacceptable risk region is set by an organization’s risk tolerance criteria
This table describes the basics of risk assessment. For example, If the risk falls into the black zone, it’s not an acceptable risk, however, in between are lots of shades of grey.
Risk analysis determines the expected frequency (or likelihood) as well as the severity for a particular consequence
Risk assessment compares the risk result level to an acceptable risk criteria
 |  | Consequences |  |  |  | 
 |  | Catastrophic | ← | Serious | ← | Negligible
Frequency | High |  |  |  |  | 
 | ↑ |  |  |  |  | 
 | Moderate |  |  |  |  | 
 | ↑ |  |  |  |  | 
 | Low |  |  |  |  | 
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Adapted from previous MINERVA Risk ppt

## Slide 89: Four Types of Risk [4]
Residual risks
  The risk you are willing to tolerate to operate your facility
  For example there is always an inherent risk will building a new fertilizer plant
Introduced risks
  Risks which are introduced during the lifecycle of a process
  New equipment or changes in personnel
Operating risks
  Risks caused by your operational procedures
Normalized risks
  Risks that are deviations from the normal risk but become normalized over time. Caused by incomplete understanding of the actual risk.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Normalized risks are things that are identified as a certain risk such as upgrading a new piece of equipment, but with time and successful operation, the perceived risk decreases.

## Slide 90: Process Hazard Analysis (PHA)
Some of the many TOOLS of PHA [1]
Simple hazard identification:
  Hazard and Operability Analysis (HAZOP)
  Failure Modes and Effects Analysis (FMEA)
  What If Studies
Simple risk analysis:
  Layers of Protection Analysis (LOPA)
  Failure Modes, Effects, and Criticality Analysis (FMECA)
Detailed quantitative risk analysis can use:
  Fault Tree Analysis (FTA)
  Monte Carlo Simulation and Markov Analysis
  Quantitative hazard effects analysis
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: An in depth look into each of the tools listed above are covered in the Hazard Assessment module (too much information to go through here) but it’s important for managers to understand the basics of each to so they will know what to do with the information.

## Slide 91: Who conducts a PHA?
The need for a PHA is usually assessed by a steering committee who have identified a need for PHA in some areas
PHAs are typically administered by a team lead
Engineers, Operations, and Maintenance staff will all be involved from necessity in generating the information required for a PHA
The team lead will gather the data and the information and recommendations are reported to management
Senior management will ultimately make a decision on any policy changes
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Also need a secretary for all meetings. These types of documents are pivotal in cases where an accident has occurred and legal action is being pursued.

## Slide 92: How do you identify hazards?
Three general categories [3]:
Logical/Rational
  Usually used for detailed PHAs
  E.g. Fault Tree Analysis is logical
Experience-based
  Moderate depth, such as checklists.
  Known scenarios maybe from historical events at the facility or similar facilities
Creative/Imaginative
  What if analysis identifies new scenarios
  Broad general PHAs require this
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Fault tree analysis – Start with an unintended state (such as release of cyclohexane gas outside it’s containment) and identify how it could get out, what would need to happen for gas to escape in those ways, and how that could come about.
What if - What if the concentration of hydroxylamine goes higher than the intended design? What if the reactor pressure gauge fails? Etc.

## Slide 93: Scope of PHAs
Although we are trying to prevent serious consequences from occurring in a process; in the PHA, the causes can be relatively minor
Does not refer to work place safety concerns such as falling off a ladder and wearing PPE, unless they are a potential cause in a larger hazard (very rare)
In general, PSM is concerned with loss of containment hazards, their causes and maintaining process integrity
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 94: Potential Process Hazards
Loss of Containment:
Chemical Release
  Spills
Energy Release
  Thermal (e.g., Fire)
  Physical (e.g., Explosion)
  Nuclear (e.g., Radiation)
Special Case – Runaway Reactions
  Thermal runaway reactions (E.g. Chemical reactions or nuclear reactions)
  A special case for the process industries which manufacture chemicals
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 95: Hazard: Chemical Release
Release of a hazardous chemical
Environmental damage
Damage to community health and welfare
tao55 / FreeDigitalPhotos.net
Sujin Jetkasettakorn / FreeDigitalPhotos.net
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 96: Hazard: Energy Release
Nuclear
Electrical
Chemical
Mechanical (kinetic)
jscreationzs/ Freedigitalimages.net
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 97: Hazard: Energy Release
An energy release from these sources can result in a:
Fire (thermal energy)
Explosion (mechanical/ kinetic energy)
  (may have many ways of starting from various sources)
Radiation (nuclear energy)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 98: Hazards: Fire
FIRE = FUEL + OXYGEN + IGNITION
Fuel:
  Volatile Liquids
  Aerosol
  Dust
Combustible aerosols and dusts can ignite more easily than some liquids.
Note, not commonly known: No liquid or solid can burn! Only the vapour on the surface of the liquid/ solid, created by heat from the ignition process, burns. The resulting fire sustains vapour development.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Aerosols and dust fueled fires and explosions are of special concern in process safety management because they are easily overlooked.

## Slide 99: Hazards: Fire
Fires are often started for free:
Heat (auto-ignition)
Open flames (welding, heaters, etc.)
Electrical (sparks, static, lightning, etc.)
tiverylucky / FreeDigitalPhotos.net
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Bottom right photo from: Image courtesy of tiverylucky / FreeDigitalPhotos.net
Ignition sources are everywhere. You should assume there is always one present

## Slide 100: Hazard: Explosion
A rapid release of energy manifested by high pressure and high temperature [4]
Chemical – Rapid oxidation reaction (often started by a flame)
Mechanical or Vapor – Sudden rupture of mechanical containment due to increased pressure or weakened container wall
Nuclear – Fission based explosion which cannot happen outside of a weapon specifically designed for this purpose (won’t happen in a nuclear power plant)
Electrical – High current electrical fault which instantly vaporizes metal and insulating materials
Magnetic – Magnetic pressure caused by ultra strong electromagnets (unlikely to happen in a chemical process plant)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Generally the first two are the most likely to happen in a chemical plant

## Slide 101: Initiating Causes
While loss of containment of chemicals and energy can lead to these hazards, often there is an initiating cause that may not be directly related:
Equipment failure
Human errors
External “acts of god”
  Inclement weather (Tornado, hurricane, etc.)
  Plane crash
  Alien invasion
  Missile Attack
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
dan/ FreeDigitalPhotos.net
Notes: Pictures are from Microsoft except the middle one.

## Slide 102: Special Case: Thermal Runaway
This is a particular worry for chemical process industries
Thermal runaway reactions are a feedback loop whereby heat is generated by a reaction which increases the reaction rate which thereby creates more heat at a greater rate, etc.
The reaction goes out of control, often resulting in an explosion
This is most often caused by failure of the process heat removal system
(Wikipedia commons)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Just a special case which causes other process hazards that is highly relevant to chemical engineers.

## Slide 103: Hazard: Runaway Reaction
“A chemical reaction process which accelerates out of control in consequence of the release of chemical energy at a rate which exceeds that which it can be removed from the system by heat transfer operations” [4]
The term “runaway reaction” is specific to reactions in vessels (because technically that definition is true for a fire)
This hazardous event has been seen in many industrial accidents and is technically avoidable with sound engineering design, but sometimes these may be caused by human factors
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 104
Hazardous Event
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Inherent Potential Hazard
Operational Defense
Prob. of failure to respond to process alarms
Initiating Causes
Freq. of initiating cause (process control failure or procedural error)
Initiating
Cause
Operational Failure
Hardware Failure
Mechanical
Failure
Loss of Containment
Hardware Failure
Prob. of mechanical integrity breach
Loss of Containment
Freq. of loss of containment
Hardware Defense
Prob. of failure of interlock and mechanical safety devices
Hazardous Event Probability and Time Line
Notes: Management made decisions that affect all levels of the organization and so they must have the correct information to make the correct choice.

## Slide 105: Using PHA information
Once you know the hazards what do you do with the information?
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 106: Management and PHAs
Management is typically not just engineers that understand the process. Decisions are made for the facility based on competing interests
PHAs that are accurate can be useful and necessary to help management from making poor decisions
Managers have to make decisions based on competing interests
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 107: Competing Interests
Finances
Productivity
Quality
Consistency
Customers
Stakeholders
Safety
Regulatory Requirements
DECISION
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 108: Engaging the workforce
Management decisions are critical [5]
Accident
Fallible Decisions
Latent
Failures
Precond-itions
Unsafe
Acts
System Failures
Hardware
Defense
Senior Mmgt
Middle Mmgt
Engineers
Supervisors
Operators
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Management made decisions that affect all levels of the organization and so they must have the correct information to make the correct choice.

## Slide 109: Risk is mutable
Assessing risk is not simple. Different people will have different opinions about severity and maybe even frequency if it not easily quantified.
Low frequency:
  Runaway reaction
  Should you protect your plant from a plane crash?
  Should you protect from natural hazards not typical to your region? (e.g., hurricanes)
  Should you protect against missile attacks?
  Should you protect against a meteorite crash?
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Anti missile units are expensive, and you probably don’t need to invest in them unless your under immanent threat of a bombing. But someone may have a different opinion on the likelihood of that event. It is difficult to quantify such low probability risks. Who is correct?

## Slide 110: Risk Management
Risk can be controlled by operating practices and process design… a.k.a
Risk Management
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 111: References
[1] Center for Chemical Process Safety. Guidelines for Risk Based Process Safety. New Jersey : Jon Wiley & Sons, 2011.
[2] Photo Credit: Tom Volk/The Morning Call. http://www.mcall.com/all-concept1,0,7393.photo
[3] Ian Sutton. (2010) Process Risk and Reliability Management: Operational Integrity Management. Elsevier.
[4] Vic Marshall and Steve Ruhemann. (2001) Fundamentals of Process Safety. iChemE.
[5] Knegtering & Pasma (2009). Safety of the process industries in the 21st century: A changing need of process safety management for a changing industry. J Loss Prevent Proc Ind. 22; 162-168.

## Slide 112: Risk Management
Operating Procedures
Safe Work Practices
Asset Integrity and Reliability
Contractor Management
Training and performance Assurance
Management of Change
Operation Readiness
Conduct of Operations
Emergency Management

## Slide 113: Risk Management
Risk can be managed in many ways. Generally the sooner in the process life cycle you implement a risk management decision, the cheaper it is.
The most cost effective time to implement safety features is during the design process
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 114: Inherently Safer Design
Use of Inherently safer design (ISD) principles seeks to avoid hazards rather than control them with added-on protective equipment [1, 2]
  Minimize:
    Reduce inventories of hazardous materials on site
  Substitute:
    Replace hazardous substances, equipment or operations with less hazardous ones whenever possible
  Moderate:
    Use less aggressive operating conditions
  Simplify:
    Only use necessary operations. Remove issues by design not by the addition of consequential process operations
Other strategies employed by ISD
  Design and locate equipment such that:
    Minimize transportation and storage of hazardous materials if possible
    Locate equipment and materials such that in the worst possible scenario the least amount of damage is done
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Intensification can lower operating costs by reducing the required facility size and construction costs or lower equipment costs for storing chemicals, etc.

## Slide 115: A tale of RISK
Once upon a time a king offered three young men an opportunity to take a chance for true love. They could open one of two doors. [1]
Behind one door was a dragon.
Behind the other was their true love.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 116: Inherently Safer Design
The first man decided not to take the risk. He lived safely until the end of his days but he never found love.
The second young men hired some risk professionals. They collected data on the tiger and the true love, built machines to detect the sounds of a dragon and calculated the probability. Naturally this took time and money and the by the time the consultants were ready to advise the man he was old and poor. Regardless he opened the recommended door and got eaten by a low probability dragon.
The third man took a course in dragon slaying.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Moral of the story: We can choose not to build or operate a process (like the first man) and we will not have to take any risks, but we will also lose the benefits. We can try to assess the risks of the process (like the second man) and try only to operate the safest possible process, but we can never be completely sure that our assessment is correct. Assessments also take time and money. But whenever possible, we should try to be like the third man. The best course of action is to the take the risk, building the process but be proactive and minimize the risks during the design stage (inherently safer design).

## Slide 117: 8. Operating procedures
This element focuses on documenting written procedures, maintaining them, and consistently using them to maintain facility integrity

## Slide 118: Three Goals
Current
Accurate
Useful
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 119: What types are covered?
Normal operations
Infrequent operations
Special high hazard procedures
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 120: Ways to write procedures [3]
Narrative
  Written in long paragraphs, difficult to follow (most common but avoid this if possible)
Paragraph
  Similar to narrative but given some structure through numbering
Outline
  Short sentences with number or indentation structure to group information
Multi-Column
  Multiple compartments of information usually used for troubleshooting guides
Flowchart
  Graphical depiction with brief descriptions
Checklist
  Basic actions with spots to initial or check off actions
Playscript
  For multiple operators that need to perform tasks together
T-Bar
  Two columns one with steps, other with details or special instructions
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 121: Contents of a Procedure
For each step in a procedure, the following should be outlined in the written protocol [3]:
  Any expected system responses (or none)
  Indicators that the step was performed properly
  Possible consequences if the step was not performed properly
  Safe operating limits
  Consequences of deviating from limits
  Any limiting conditions
  Address what procedure should be followed if deviations from the limits is detected
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: A limiting condition could be that you cannot unload flammables during a lightning storm. If deviating from the limit of a reaction at 90C, then the operator might be instructed to start an additional cooling pump.

## Slide 122: Validation & Maintenance
Written operating procedures must be used consistently, therefore it is important to validate that they conform to the actual procedures used. [3]
However, the correct and safe practice should be the one finally reflected in the procedure and should be implemented if not in actual practice. Once they are implemented, ask for feedback from the operators to correct any errors or omissions.
Procedures must be available to those using them and those you may need to use them infrequently.
They should be updated & reviewed regularly
Old procedures must be controlled to ensure that only the correct practices are being used.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: For example, an old procedure for an autoclave was posted beside the autoclave. The operating used these instructions, not the current ones available on the companies intranet to operate the autoclave and severely burnt themselves by incorrectly sealing the chamber.

## Slide 123: 9. Safe work practices
This element focuses on using safe work procedures during maintenance or non-routine work.

## Slide 124: Non-routine work
This does not refer to the frequency of the task
Any work that is not a part of the normal operating process [3]:
  Inspections
  Calibrations
  Repairs
  Testing
  Maintenance activities (specific procedures are covered in the maintenance element)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 125: Cover all your bases
Three sets of procedures will help cover all possibilities and reduce risk:
Operating procedures (Element 8)
  Normal process operations
Safe work practices (Element 9)
  Non-routine work
Maintenance procedures (Element 10)
  Maintenance of equipment (routine but not part of normal operations)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 126: Work Permits
Non-routine work should use a permit system which must be authorized and confirmed with the correct personnel prior to the activity being undertaken [3]
  Operators
  Technicians Performing Work
Permits are updated at each shift change
Permits also ensure the appropriate locks on valves or switches are in place prior to the work taking place
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 127: Other Things Work Permits Control
Permits will require that safe work procedures are used and this may involve placing a fire blanket when welding to prevent ignition, for example [3]
Confined space entry
Hot work (Fire hazard)
  Welding, cutting with no fuel source present
  When flammables are present, welding, drilling, grinding become an ignition hazard
Opening vessels, lines, etc.
Lock outs (electrical, valves. etc.)
Construction (inside or adjacent to operating areas)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Construction can affect operations in many ways from creating ignition sources to lifting over vessels or equipment to excavating near underground lines, etc.

## Slide 128: Piper Alpha Oil Platform Explosion, 1988
The explosion at Piper Alpha was caused by improperly managed safe work practices for example, safety valve inspection/ testing.
  An offshore oil rig exploded resulting in 167 deaths and $1.7 B dollars in damage [3]
  The explosion was caused by a hydrocarbon leak due to the removal of a safety valve on a pump which was removed for inspection/ testing and not reinstalled prior to the shift change.
  The pump had been taken out of service earlier that day for maintenance work
  The night crew was aware of the maintenance work and had to authorize electricians to resupply the pump with power in order to return it to service
  It is unclear if the night crew knew that the maintenance was incomplete
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: “The incident was caused by the night crew putting a condensate injection pump into service that, earlier in the day, had been taken out of service for maintenance. The night crew was aware of the maintenance activity and, in fact, had to authorize the electricians to close the switch at the motor control center so that the pump could be returned to service. The evening shift operators were likely told that all of the maintenance work scheduled to be performed by the maintenance group was either complete or had been deferred however, they were not aware that other work being
performed by a contractor was incomplete. In fact, the contract crew had removed a pressure safety valve on the pump discharge line for recertification and was unable to return the valve to service prior to 6 p.m. when they quit for
the day. Once the pump was started, a large release of hydrocarbons ultimately led to the disaster” [2]

## Slide 129: 10. Asset integrity and reliability
This element focuses on the design, installation and maintenance of equipment from when it is fabricated to its retirement to ensure it is fit for use

## Slide 130: Critical Element
VERY important element
Covers a major desire in process safety:
MAINTAIN PROCESS INTEGRITY
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 131: Equipment Failure
This has been a leading cause of accidents in the process industries [3]
  Poor design
  Poor installation
  Poor maintenance
    Undetected deterioration
    Improperly performed maintenance
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 132: Managing asset integrity
  Inspections
  Testing
  Certifications
This is one of the two primary responsibilities of a process facility [3]:
Preventing a loss of containment incident
Ensure the dependability of critical systems that prevent these types of events
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 133: American Airlines Flight 191, 1979
Deadliest air crash in the US, 273 fatalities [1, 4]
Caused by improper maintenance procedures
In an attempt to save time and money, the airline instructed maintenance mechanics to remove the engine and pylon together instead of doing it separately as indicated in the maintenance procedures
This resulted in a damaged pylon that was undetected for several flights
During the final takeoff, the pylon failed and the wing was ripped off during takeoff causing the crash
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Improper maintenance accidents are not limited to chemical process plants. It was lucky the plane crashed in an area with little personnel. Two people on the ground were killed, but it could have been far worse if the plane had crashed into the airport terminal. An investigation later revealed that many DC-10 airplanes had been subject to the same faulty maintenance procedure and so the procedure banned. Photo from Wikipedia Commons - Source: United States Federal Aviation Administration

## Slide 134: 11. Contractor management
The purpose of contractor management is to ensure that contract workers work according to safe work practices and that they don’t increase the operational risk of the facility

## Slide 135: Why are contractors used?
Specialized skills
Maintenance and Repairs
Construction
Equipment Installation
Janitorial Work
Grounds keeping
Many other reasons
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[3]
Notes: This element is becoming increasingly important as contracting services is becoming more common. They might be contracted for a variety of reasons like limited resources that cannot supply full time staffing but can hire staff for periods of unusual demand etc. Outsourcing work is becoming more common way of saving money in tight times. But temporary workers can increase the risk if they are granted access to hazardous systems areas or they are working at a busy time such as a shut down for maintenance. They may actually bring in new hazards with them like x-rays, unique chemical hazards, etc. [2]

## Slide 136: Process of Contracting
Selection
Acquisition
Use (& Training)
Monitoring
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
[3]
Notes: Need to have policies for all of these things. Training is going to be different for contractors (short-term employees) than employees so special attention is required to establish the training policies. Sometimes the contractor will be the one providing the training to employees if they are bringing in new hazards.

## Slide 137: Contractor Management System
Prequalify accredited firms
  Safety record
  Strong safety culture
  Employee turnover rate
  Previous performance
Encourage near-miss reporting among contractors. They are the least likely to do so and most likely to get hurt on the job [5]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 138: Piper Alpha Continued [6]
The safety valve which was removed earlier, was removed by a contractor that had been hired to inspect/ test it.
The contractor had not been trained properly in the safe work practices needed for the task.
The incident investigation also determined that the inadequate emergency response training given to contractors on the rig contributed to the high loss of life
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 139: 12. Training and performance review
Training is required to ensure that workers preform a task to a minimum standard, to maintain their proficiency, or to upgrade their skills. Performance reviews determine when these actions are required.

## Slide 140: What is training?
Practical instruction in job tasks or methods [3]
Enable workers to meet minimum performance standards
Performed before the worker is allowed to perform the task on their own
Followed by performance assurance to confirm that the worker is performing the tasks correctly and that they posses the knowledge, skills, and abilities (KSAs) required for their position
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 141: Developing new training
Start by identifying the KSAs you are trying to develop [3]
Identify or hire qualified personnel to develop the materials.
Procure training materials
Develop training program/ course
Develop ways to assess the KSAs post-training
Validate the training by getting feedback from workers that are currently considered qualified
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 142
Job or Task Analysis
Job Requirements
Gap Analysis
Develop Training Program/ Course
Training
Assess KSAs
Reassign Worker
Adapted from [3]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Incident Investigation
New Regulations
Auditing
Management Review
Organizational Change
Other Elements
Inadequate Learning Ability
Adequate Learning Ability, periodic refresher training

## Slide 143: 13. Management of change
This element proscribes a system for dealing with all types of modification at a facility from chemical supplier changes, facility changes, to personnel changes

## Slide 144: One of the most important elements
Management of change (MOC) is critical for preventing changes from increasing the facilities risk of a loss of containment event
MOC also helps a facility remain in compliance with government regulations, the Responsible Care initiative, and helps maintain other quality initiative like ISO 9000 [7,8]
MOC interacts with almost every other element in the risk management area and also the knowledge management element in the hazard assessment section
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 145: Example process
A change request is made [7, 8]
Qualified independent personnel (i.e. not the requestor) review the request to identify any additional hazards
The responsible party either reject or approves the request based on the review
If it is approved it can be implemented
Prior to implementation the relevant operating procedures or process safety documentation is updated and the potentially affected personnel are informed
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 146: Process Life Cycle
Process Development
Detailed Design
Construction
Startup
Operating lifetime
Extended Shutdowns
Decommissioning
Many changes will occur throughout the lifecycle of a process facility. The general stages are shown above. [3, 7, 8]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 147: Emergency Changes
Sometimes emergency changes are necessary. [7, 8]
  Change must be implemented to prevent an environmental release
  Correct a deficiency that an immediate threat to the safety of workers
  The facility must be prepared for an external threat (for example a tidal wave or flood)
Therefore it is useful to have an expedited system. However to prevent unessential use of the system, it should be a requirement to complete the full request for change process as soon as possible afterward.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 148: 14. Operational readiness
This element covers processes for conducting pre-startup reviews of new processes or processes that were temporarily out of service

## Slide 149: Readiness
Processes should be shutdown in a way to confirm they are safe to restart later [3]
Duration of shutdown should be a factor in the safety verification
Consider any modifications that we necessary for shutting down the process
Likelihood of having an accident is highest during process transitions such as shutdowns and startups
A readiness record makes it easy to audit a process later and determine potential issues
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Pictures from microsoft

## Slide 150: Prior to startup (old & new processes)
Verify current condition with equipment or design specifications [3]
Ensure all process procedures are in place
  Operating procedures
  Safe work procedures
  Emergency procedures
  Maintenance procedures
Ensure training is completed by operators which may affect the process
Confirm the process is safe to operate
  Inspections
  Cleanliness
  Isolation from potential hazards, etc.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 151: Readiness Review
Verify [3] :
  Equipment readiness (meets design specs)
  Process control systems
  Emergency shutdown systems
  Cleaning processes have been complete (if applicable)
  Equipment lineup is validated
  Procedures are in place
  Emergency response equipment is in place
  Training is up to date for all operators that may affect the process
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 152: New Processes
Have undergone full management of change request & approval process [3]
  All documentation has been updated
  PHA, where necessary, has been completed
  All equipment or safeguards have been installed
Conduct pre-startup review prior to starting the process
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 153: 15. Conduct of operations
This element focuses on operational discipline. This element is extremely important in a field which is dependent on operators performing their tasks correctly every time.

## Slide 154: Tied to Organizational Culture
Workers are expected to perform with [3]:
  Alertness
  Due thought
  Full knowledge
  Sound judgement
  Sense of accountability
A workers ability to perform their tasks perfectly repeatedly is dependent on the culture of the organizations
Mistakes cannot be tolerated in an environment where small deviations could lead to catastrophic results
Formal operational activities are increasingly required for consistent performance in complex systems
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Safety culture is critical and is tied to accountability. If a manager praises an operator who “waits it out” to avoid a shutdown of the process, then operators who follow operational protocol while suffer low morale. They will be encouraged to deviate from the defined procedures. Therefore, management must be aware of their behaviour and the effects on employees. They should not tolerate ANY DEVIATION from the approved procedures even for inconsequential or positive deviations.

## Slide 155: Accountability
Reliable and consistent operations will also benefit product quality and productivity
The conduct discipline culture should acknowledge that humans do err. However, it is due to this fact that there is a need to detect these errors and also develop safeguarding systems to prevent them from becoming an accident [3]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Picture is from Bing Search using creative commons license as a search parameter (from Finnish Wikipedia).

## Slide 156: Conduct Consequences
Applies to all workers (management, contractors, operators, engineers, etc.) [3]
Often tied close to human resources personnel:
  Fitness of duty assessment
  Disciplinary actions
  Salary & bonuses
  Retention decisions
Authority, accountability and work performance indicators should be defined
  May be coordinated with other element outputs
    Equipment status for asset integrity
    Near miss reports for incidents element
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 157: 16. Emergency management
The emergency management element involves planning for emergencies, practicing them, training employees, contractors and local authorities, as well as communicating with local stakeholders.

## Slide 158: Objectives
Protect people onsite and offsite including emergency responders [3]
  Planning & training
  Drills
Communicate with stakeholders before an incident
  Planning & coordination
Communicate with the media in the event of a serious incident
  In conjunction with the stakeholder communication element (element # 5)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 159: Protecting people
Planning
  Create emergency procedures such as shutdown, isolation of hazardous materials [3]
  Create emergency evacuation plans
  Assess the need for emergency management equipment on site such as:
    Blast walls
    Fire fighting equipment
    Plant alarms, etc.
Training
  Train all staff and contractors on the developed procedures and facility evacuation plan
Drills
  Periodically test the readiness of the operators and contractors to safety shutdown and evacuate the facility
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 160: Coordination with Municipal Crews
Planning
How much a facility will want to depend on municipal emergency responders [3]
Preventative vs. Mitigative safeguards
  Regain control with preventative safeguards to prevent incident
  Reduce impact of incident with mitigative safeguards
Communication
Make important information available to municipal crews to protect their safety if an incident occurs (flammables on site, toxic fumes, etc.)
Establish a system for ensuring a quick response in the event of an incident
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Some facilities will decide that they rather spend their resources on preventing an incident than buying fire fighting equipment (for example). There is a balance between dealing with the consequences and preventing it from ever happening.

## Slide 161: Scope
Emergency management will involve many people from all levels of the organization [3]
Immediate actions will be taken by operators:
  Shutdown the process
  Isolate hazardous materials
Further actions will be coordinated by an incident commander
  Coordination of specialist teams such as HAZMAT or Fire fighters
  Order evacuation
  This person should have experience in emergency decision making
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Photo from Wikipedia commons (Department of Justice Website US). Oftentimes operators might have a better understanding of the process compared to local crews, however, because they feel some ownership to the process and their organization, biased decisions can be made which might lead them to take unacceptable risks. Therefore a incident commander with some training in emergency responses should be used in the event that the incident is not put under control by the immediate actions of the operators (as they have been previously trained to do.) Picture from microsoft

## Slide 162: In the event of an incident
An effective emergency management system will do the following things in the event of a loss of containment incident [3]:
Save lives
Protect property & the environment
Reassure stakeholders that the facility is properly managed and should be allowed to continue operating
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 163: Emergency Management Systems (EMS)
Required by law:
Canadian Environmental Protection Act (CEPA)
Good business Sense:
Damage to reputation
  Customers
  Employees
  Community
Cleanup costs
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Reputation with customers will affect your profits. You want to maintain a reputation that you care for your employees and your facility is safe. You want to community to work with you in the future, not against you. Picture from Microsoft.

## Slide 164: Piper Alpha Continued
Loss of life may not have been so high if more effective emergency management was present [3]:
All personnel authorized to order evacuation were killed in the first blast.
  This was due to the fact that the control room where they were located did not contain any blast walls. Poor emergency management design
  Personnel with authorization to evacuate the facility should not be located together
The workers who did not evacuate and were sheltered in the galley were all killed
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: There has been some controversy as to whether the loss of life of the Alpha Piper incident would have been so high if there was a more effective emergency management system
Personnel authorized to order evacuation were killed in the initial blast. No blast walls were present in the control room where they were located. Poor engineering design.
Operators of the other platforms were unclear of the appropriate action after they were aware the first platform was burning
Therefore they did not shut down or isolate the hazardous materials after the incident occurred.
This lead to the second explosion. Lack of procedures.
Workers were not ordered to evacuate and many instead sheltered in the galley and were not rescued
Helicopters and other fast evacuation methods were prevented by the enormous flames

## Slide 165: Piper Alpha
Operators were not aware of any procedures to shutdown the process or isolate the hazardous materials [3]
  Operators did not believe they had the authority to shut down the process even though they could see the rig was on fire
  This was the direct cause of the second explosion
  This was due to a lack of emergency procedures
Evacuation routes were blocked by enormous flames (helicopters)
  Lack of coordination with government emergency crews
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Photo of boat from fotopedia.com (Other from Microsoft)

## Slide 166: References
[1] Trevor Kletz. Plant design for safety: a user friendly approach. Hemisphere Publishing Corporation: New York, 1991.
[2] Trevor Kletz. Process Plants: A Handbook for Inherently Safer Design. CRC, 1998.
[3] Center for Chemical Process Safety. Guidelines for Risk Based Process Safety. New Jersey : Jon Wiley & Sons, 2011.
[4] National Transportation Safety Board. Aircraft accident report: American Airlines, Inc. DC-10-10, N110AA. Chicago O'Hare International Airport Chicago, Illinois, May 25, 1979. Report 20594, 1986.
[5] Center for Chemical Process Safety. Guidelines for Management of Change. New Jersey : Jon Wiley & Sons, 2008.
[6] Oil & Gas UK. Piper Alpha: Lessons Learnt, 2008.
[7] Chitram Lutchman, Rohanie Maharaj, & Waddah Ghanem. Safety Management: A comphrensive approach to developing a sustainable system. CRC Press: Florida, 2012.
[8] Center for Chemical Process Safety. Guidelines for Management of Change. New Jersey : Jon Wiley & Sons, 2008.

## Slide 167: Enhancing PSM
Incident Investigation
Measurement and Metrics
Auditing
Management Review and Continuous Improvement
Implementation

## Slide 168: Continuous improvement
The most effective PSM systems use new information as it becomes available over the lifetime of the process to continuously improve the PSM system [1]
Enhancing PSM is based on learning from experience
This is typically done through:
  Investigating incidents or near misses that occur and addressing their root causes
  Apply lessons learned from other similar facilities
  Measuring performance
  Auditing the PSM system
  Performing management reviews

## Slide 169: 17. Incident Investigation
As it sounds, this element is about investigating any incidents or near misses to determine the root cause (if possible) and applying this information to improve the PSM system

## Slide 170: Process
Formal accident reporting, tracking, and investigation system [1]
Analyzing incident trending
Learn from experience – apply newly acquired information if appropriate
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 171: Organization Culture
This system is not for blaming employees and results should not be treated as such [1]
It should be approached as a mechanism for addressing the underlying system procedures or process cause
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Playing the “blame game” makes people less forthcoming in reporting incidents or near misses, and giving accurate accountings of incidents that have occurred. Recommendations after the investigation is complete will therefore be ineffective at preventing future incidents. Therefore it should be treated like the operator did not have the full training or correct operating procedures of what to do in that situation and so the system must be improved to prevent such an event in the future.

## Slide 172: 18. Measurement & Metrics
This element focuses on measuring and assessing the actual performance of a process and not the intended performance which may become misleading over time.

## Slide 173: Metrics
Metrics are indicators of system performance [2]
  Incidents frequency is not effective indicators for proactive process improvement
  It is often used for reactive process improvement, however, proactive prevention should be best practice
Types of measurements and frequency of updating indicators is facility and process specific
  Depends on cost, local needs, the type of process, risk level, operational dynamics, commitment to process safety
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Incidents do not occur frequently enough to be helpful in assessing the effectiveness of the process safety management system. It is analyzed during the Incident Investigation element #17. How often metrics are refreshed is highly dependent on safety culture in the facility. If PSM is strictly adhered to and process fluctuations are uncommon then metrics will not require as high of a sampling frequency. Picture is from microsoft

## Slide 174: KPIs
There may be some mandatory requirements for KPIs for a particular process or piece of equipment and this should be taken into account.
This element can often be combined with other business metrics such as efficiency, cost analysis, and productivity
Easier to take corrective actions proactively, therefore use leading indicators [2]
  We call these Key Performance Indicators (KPIs)
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: picture from Microsoft

## Slide 175: Leading & Lagging Indicators
Leading
Input measurements which are typically hard to measure but easy to influence. This type of improvement is pro-active [1]
Measures the barrier’s strength and maintains it to prevent incidents in the Swiss Cheese Model of PSM failure
Lagging
Output measurements that are easy to measure but difficult to improve. This type of improvement is reactive
Measures the protective barrier defects and the events and consequences in the Swiss Cheese Model of PSM failure
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Near-Miss reporting is an example of both leading and lagging because you use the information from the incident investigation to strengthen your layers of protection, but you are also recording a lagging output measurement of the system performance.

## Slide 176: Example – Losing Weight
Indicators
Which is leading/lagging [2]?
Weighing yourself on a scale
  Easy to measure
  Difficult to take corrective action
Counting your consumed calories and your expended calories
  Difficult to measure
  Easy to take corrective action
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Picture is from microsoft.

## Slide 177: Documenting & Reporting
Long term documentation is dependent on [2]:
  Process risk
  KPI measurement Regulatory requirements
Often, government or professional associations (such as Responsible Care) will require the reporting of some KPIs
This allows them to develop new metrics or recommendations for all facilities in order to improve the safety of whole industries
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: KPIs can be used to report performance and remind workers of the deviations from the expected as workers may become complacent if an accident has not occurred recently. Picture from “Presto Writes. http://prestowrites.wordpress.com/”

## Slide 178: 19. Auditing
This element is critical in assessing the effectiveness of the PSM system. It should identify weaknesses in the design or implementation, and use this information to correct them.

## Slide 179: What is an Audit?
Independent
Systematic
Comparison of current process to Standards of Care
  Guidelines which include standards, regulatory requirement and other external rules
  Internal self-imposed requirements
Auditing is most often used during the operating phase of a facility
[1]
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: Auditing is used during all phases of a process’s lifecycle, such as auditing designs to give an independent assessment of their suitability. There might be some laws or regulatory requirements on the scope and timing of audits which must be taken into account. Picture from Microsoft.

## Slide 180: Frequency
How often audits are conducted will depend on several factors [1]:
Process inherent risk
Phase process life cycle
Past experience
Maturity of the PSM system
Maturity of organizational culture
Facility, corporate, or regulatory requirements
Regardless, some audits should be conducted on a regularly scheduled basis such as once a year
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 181: Who & How? Scope
Team based activity [1]
  However, requires access to operators and experts
  Team should be lead by competent personnel
Element by element (typically)
Directed primarily by documented protocols
Physical Scope – What element or units are being audited?
Analytical Scope – What are the auditing criteria?
Temporal Scope – What time period are you auditing? E.g. April 1, 2013 - March 30, 2013
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: If your audit team is not competent you might as well not audit your process. The senior team leader should be familiar with the auditing process and requirments, strong organizational abilities, a good sense of curiosity, possess tact but also confident and able to deal with confrontation/rebuttal [2]. Teams help newer auditors improve their abilities through mentorship and guidance and provide a more comprehensive perspective. Often, auditors will be contracted from outside firms which are specialized, chosen from corporate headquarters, or chosen from other facilities to increase objectivity. Auditors when chosen “in-house” might be more accustomed to the status-quo. Some facilities use a hybrid team of objective (contractors, outside personnel) and familiar auditors (in house personnel) to work together.

## Slide 182: Implementing Audit Findings
Audits are not useful on their own [1]
Findings must be used to improve PSM
  Adopt as proposed
  Adopt in principle (the recommendation will be implemented in an equivalent manner)
  Reject based on the assertion that the recommendation was made in error (Because of an error in facts or in judgement)
  Reject due to a change which has rendered the recommendation inapplicable.
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: recommendations may still need to go through management of change requests if they are to do with the process. Management of the elements may be easier to implement.

## Slide 183: 20. Management Review and Continuous Improvement
This element focuses on the routine review of management systems for effectiveness and ability to produce the desired results

## Slide 184: What is a management review?
Like an audit, but less formal, more frequent, and the reviewers are generally in-house employees
Breakdowns in management systems are harder to detect and slower to be noticed
For example:
  The training coordinator unexpectedly leaves
  The trainers continue to train people and the element seems intact
  A management review revels that some workers or contractors are overdue for training
  At that point it could be too late…
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 185: Hot work Explosion, Delware, 2001
Catwalk above sulphuric acid tank needed welding repair. The sulphuric acid tank below had holes and was in a poor state of repair [1,3]
1 contractor killed and 8 others injured as a result of the explosion
Large volume of sulphuric acid was released into the environment
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM

## Slide 186: Root Cause
Management Review
Hazards were not assessed correctly since the tank was changed from normal acid service to spent acid service (corrosivity & flammability hazards changed) [1]
Sulphuric acid tanks were not maintained properly and requests for maintenance were always ignored or deferred
Previous requests for hot work were denied due to toxic and sufficient flammable gas concentrations
The hot work permit did not specify atmospheric monitoring despite previous permits being denied for this reason
Introduction
Commitment to PSM
Hazard & Risk Assessment
Risk Management
Enhancing PSM
Notes: These are all breakdowns in the management system. If a review had been conducted it would have been found that the PSM elements were not working together.

## Slide 187: Remember – The elements work together!
[1,4,5,6]

## Slide 188: References
[1] Center for Chemical Process Safety. Guidelines for Risk Based Process Safety. New Jersey : Jon Wiley & Sons, 2011
[2] Karel van der Poel. Lagging and leading indicators. http://kpilibrary.com/topics/lagging-and-leading-indicators Accessed Nov 9, 2013.
[3] U.S. Chemical Safety and Hazard Investigation Board. INVESTIGATION REPORT. REPORT NO. PB2002-108210. http://www.csb.gov/assets/1/19/Motiva_Final_Report.pdf Accessed Nov 9, 2013.
[4] Trevor Kletz. Plant Design for Safety: a user friendly approach. Hemisphere Publishing Corporation, 1991
[5] Canadian Society for Chemical Engineering. Process Safety Management Guide. Ottawa : Canadian Society for Chemical Engineering, 2012.
[6]. Energy Institute. High Level Framework for Process Safety Management. London : Energy Institute, 2010.